Scaling Definitions

1) Consensus (Old)

Define

ZM = 300000 bytes ; Minimum penalty free zone.

MB = Block weight in bytes.

ML = The median over the last 100000 blocks of max((min (MB , 1.7ML), ZM , ML/1.7) ; recursive calculation for ML with ML starting at ML of previous 100001 block (currently = ZM); Long term median

ML ; Dynamic penalty free zone.

MS = the median over the last 100 blocks of max(MB , ML) ; Effective short term median.

MN = min(MS , 50ML) ; Median for Penalty calculation.

RBase = Block Reward.

0 < MB ≤ 2MN ; Requirement for a valid block.

B = MB /MN - 1 where -1 < B ≤ 1

PB = RBaseB2 for B > 0 ; Monero applies a penalty PB, to increase the block weight by B; PB = 0 for B ≤ 0

Proposed Scaling Definitions (November 2025 update)

1) Consensus (New)

Define

ZM = 1000000 bytes ; Minimum penalty free zone.

MB = Block weight in bytes. For transaction weights see section 5.

ML = The median over the last 100000 blocks of max((min (MB , 2ML), ZM , ML/2) ; recursive calculation for ML with ML starting at ML of previous 100001 block (currently = ZM); Long term median

ML ; Dynamic penalty free zone.

MS = the median over the last 100 blocks of max(MB , ML) ; Effective short term median.

MN = MS ; Median for Penalty calculation.

RBase = Block Reward.

0 < MB ≤ min(2MN , 16ML) ; Requirement for valid block.

B = MB /MN - 1 where -1 < B ≤ 1

PB = RBaseB2 for B > 0 ; Monero applies a penalty PB, to increase the block weight by B; PB = 0 for B ≤ 0

Changes

1) The requirement for a valid block is now 0 < MB ≤ min(2MN , 16ML). This caps the maximum MB to 16ML as opposed to 32ML. It also means that the maximum allowed MB is reduced for MS > 8ML. For MS = 16 ML, MB is capped by MS
2) Maximum growth of MS is reduced from 50ML to 16ML and maximum growth of MB is reduced from 100ML to 16 ML.
3) Rate of growth and decline of ML is increased from 1.7x to 2x
4) ZM is increased from 300000 bytes to 1000000 bytes

Note 1: (Optional) Transitional Hard Fork Keeping RingCT

The above can be implemented as a transitional stage 1 hard fork with the current RingCT using ZM = 250000 bytes. On the stage 2 hard fork for FCMP++ the only consensus change that is then needed is to multiply the ZM constant by 4. This allows for a 4000000 byte maximum on ramp to 50000 blocks to address the current code constants vulnerability.
2a) Minimum Fee For Node Relay (Old)

We add a, penalty attracting, transaction T with a size of TT to a block of weight MB

Define

TR = 3000 bytes ; Reference Transaction weight. Note: TR must be greater than T2. T2 equals the weight in bytes of a 2 input and 2 output transaction.

BT = TT / MN

PBT = RBase(B+BT)2 = Rbase( B2 + 2BBT + BT2 ) ; The new penalty, where B + BT > 0

PT = PBT – PB = RBase(2BBT + BT2 ) ; Increase in penalty from adding transaction T

FT = RBase(2BBT + BT2 ) ; The additional fee required to overcome the increase in penalty PT

For the case B = 0 this reduces to FT = RBaseBT2

MF = ML ; Median for minimum fee calculation
To calculate the minimum fee we consider a transaction of weight TR at the start of the penalty, B = 0 with MN = MF 95% of the fee required to pay the penalty incurred is the minimum fee.

BRL = TR / MF ;

FR = RBaseBRL2 ; Fee required to pay the penalty incurred

fR = RBaseBRL/MF ; Fee required to pay the penalty incurred per byte for a given MF

fI = 0.95fR ; Minimum fee per byte

2a) Minimum Fee For Node Relay (New)

We add a, penalty attracting, transaction T with a size of TT to a block of weight MB

Define

TR = 10000 bytes ; Reference Transaction weight. Note: TR must be greater than T2. T2 equals the weight in bytes of a 2 input and 2 output transaction.

BT = TT / MN

PBT = RBase(B+BT)2 = Rbase( B2 + 2BBT + BT2 ) ; The new penalty, where B + BT > 0

PT = PBT – PB = RBase(2BBT + BT2 ) ; Increase in penalty from adding transaction T

FT = RBase(2BBT + BT2 ) ; The additional fee required to overcome the increase in penalty PT

For the case B = 0 this reduces to FT = RBaseBT2

MF = ML ; Median for minimum fee calculation

To calculate the minimum fee we consider a transaction of weight TR at the start of the penalty, B = 0 with MN = MF 100% of the fee required to pay the penalty incurred is the minimum fee.

BRL = TR / MF ;

FRL = RBaseBRL2 ; Fee required to pay the penalty incurred

fRL = RBaseBRL/MF ; Fee required to pay the penalty incurred per byte for a given MF

fIL = fRL ; Minimum fee per byte

Note 1: Transitional Hard Fork (Implications)

TR = 2500 bytes or 5000 byes if note 2 below is chosen for FCMP++.

Note 2: (Optional) Double fees

Increase TR to 20000 bytes.

Note 3: (Optional): Additional, minimum fee, per byte for large transactions.

fIN = 4fIL, If a transaction has a weight TT > 20000 bytes
and / or more than 8 inputs.

Changes

1) TR is increased from 3000 bytes to 10000 bytes. For clarity TR is defined outside of consensus.
2) There is no reduction to 95% of the minimum fee. This is all now handled on the wallet side.
2b) Wallet Fees (Old)

For the calculation of wallet fees we assume that the next 10 blocks have no transactions, other than the coinbase transaction, the empty blocks, We then calculate MLW and MSW by following the calculation of ML and MS at this future point. We use the previous 99990 blocks and the future 10 empty blocks (100000 blocks) for ML and the previous 90 blocks and future 10 blocks (100) blocks for MS.

Define

MBW = MB for the last 99990 blocks
MBW = 0 for the future 10 blocks; A value of 0 bytes can be used for the empty blocks for the purposes of calculating MLW.

MLW = The median over the last 99990 blocks and future 10 blocks (100000 blocks) of max((min (MBW , 2ML), ZM , ML/2) ; The current value of ML from consensus is used; Effective long term median for wallet fees

MLW ; Penalty free zone for wallet fees

MSW = the median over the last 90 blocks and future 10 blocks (100 blocks) of max(MBW , MLW); Effective short term median for wallet fees

MNW = min(MSW , 50MLW)

MFW = MLW ; Median for wallet fee calculation

BRLW = TR / MFW ; Used for the low and normal fees

BR = TR / ZM ; Used for the medium and high fees

FL = RBaseBRLW2 ; Low transaction fee for reference transaction

fL = RBaseBRLW/MFW ; Low transaction fee per byte for a given MFW

fN = 4fL ;Normal transaction fee per byte for a given MFW

fM = 16 RBaseBR/MFW ; Medium Transaction fee per byte for a given MFW

fP = 2RBase/MNW = fMMFW/(8BRMNW); Maximum Penalty (B =1) Transaction fee per byte for a given MNW

fH = 4fMmax (1, MFW/(32BRMNW)); High Transaction fee per byte

2b) Wallet Fees (New)

For the calculation of wallet fees we assume that the next 1000 blocks have no transactions, other than the coinbase transaction, the empty blocks, We then calculate MLW by following the calculation of ML at this future point. We use the previous 99000 blocks and the future 1000 empty blocks (100000 blocks) for ML.

Define

MBW = MB for the last 99000 blocks
MBW = 0 for the future 1000 blocks; A value of 0 bytes can be used for the empty blocks for the purposes of calculating MLW.

MLW = The median over the last 99000 blocks and future 1000 blocks (100000 blocks) of max((min (MBW , 2ML), ZM , ML/2) ; The current value of ML from consensus is used; Effective long term median for wallet fees

MLW ; Penalty free zone for wallet fees

MFW = MLW ; Median for wallet fee calculation

BRLW = TR / MFW ; Used for the low, normal and medium fees

BR = TR / ZM ; Used for the high and maximum fees

FL = RBaseBRLW2 ; Low transaction fee for reference transaction

fL = RBaseBRLW/MFW ; Low transaction fee per byte for a given MFW

fN = 4fL ; Normal transaction fee per byte for a given MFW

fM = 16fL ; Medium Transaction fee per byte for a given MFW

fH = 64 RBaseBR/MFW ; High Transaction fee per byte for a given MFW

fX = max(2RBase/MFW , 4fH) Maimum transaction fee per byte. This is greater than or equal to Maximum Penalty (B =1 ) Transaction fee per byte for a given MFW

Changes

1) All fees including the high fee are now based upon MLW
with the ratio between fees constant for a given MLW.
2) The grace period is increased to 1000 blocks.
3) 5 fee levels with at least a 4x factor between fees.
3) Transitional considerations for Minimum penalty free zone, ZM, and Median calculations after the fork.

Define:

ZMOld = 300000 bytes (ZM before hard fork)

MBOld = Block Weight in bytes (before hard fork)

3) Transitional considerations for Minimum penalty free zone, ZM, and Median calculations after the fork.

Calculation of ML, MS, MLW and MSW where blocks from a previous the Monero version are included in a calculation after the fork. MB is modified as follows:

Define

ZM = 1000000 bytes

For blocks before the hard fork
MB = MBOld ( ZM / ZMOld )

The medians are then calculated normally.

Note 1: Transitional Hard Fork (Implications)

Apply the transitional considerations for each hard fork:

1) ZMOld = 300000 bytes, ZM = 250000 bytes
2) ZMOld = 250000 bytes, ZM = 1000000 bytes

4) Wallet Fee Rounding

Wallet fees, fN, fL, fM, and fH are rounded up to the desired
number of significant digits in the significant

Wallet Fee Rounding Examples

Two significant digits

27810	Rounded to : 28000
37.94	Rounded to : 38
0.5555	Rounded to : 0.56
0.002342	Rounded to : 0.0024
4) Wallet Fee Rounding

Wallet fees, fN, fL, fM, fH, and fX are rounded to 2 significant digits in the significant

Wallet Fee Rounding Examples

Two significant digits

27810	Rounded to : 28000
37.94	Rounded to : 38
0.5555	Rounded to : 0.56
0.002342	Rounded to : 0.0023
5) Transaction Weights

Transaction weighs are used to account for the different growth rate the output proof verification time with the number of outputs. This is done at consensus level and can lead to double charging if the fee per byte rate is increased because of an increase in the transaction weight.
5) Transaction Weights (Proposed)

Breakdown of the transaction weights as follows:

Use a standard weights roughly based upon the current size in bytes. Calculation based upon the number of inputs and 2 outputs. Then three additional weights are added to the 2 output weights for outputs greater than 2 as follows:

a) 3 or 4 outputs: The additional weight added is based upon the average increase in size over inputs of 4 outputs over 2 outputs.

b) 5, 6, 7 or 8 outputs: The additional weight added is based upon the average increase in size over inputs of 8 outputs over 2 outputs.

c) 9, 10, 11, 12, 13, 14, 15, 16 outputs: The additional weight added is the average increase in size over inputs of 16 outputs over 2 outputs.

A standard weight for the fee is implicit. This is minimal and will avoid the need to do recursive wallet fee calclations.

d) TX extra will have a weight equal to its size, that is added on.

The weights will be Itemized in a spreadsheet to follow.