Scaling Definitions

1) Consensus (Old)

Define

ZM = 300000 bytes ; Minimum penalty free zone.

MB = Block weight in bytes.

ML = The median over the last 100000 blocks of max((min (MB , 1.7ML), ZM , ML/1.7) ; recursive calculation for ML with ML starting at ML of previous 100001 block (currently = ZM); Long term median

ML ; Dynamic penalty free zone.

MS = the median over the last 100 blocks of max(MB , ML) ; Effective short term median.

MN = min(MS , 50ML) ; Median for Penalty calculation.

RBase = Block Reward.

0 < MB ≤ 2MN ; Requirement for a valid block.

B = MB /MN - 1 where -1 < B ≤ 1

PB = RBaseB2 for B > 0 ; Monero applies a penalty PB, to increase the block weight by B; PB = 0 for B ≤ 0

Scaling Definitions (17th December 2025 MRL meeting)

1) Consensus (New)

Define

ZM = 625000 bytes ; Minimum penalty free zone.

MB = Block weight in bytes.

ML = The median over the last 100000 blocks of max((min (MB , 1.2ML), ZM , ML/1.2) ; recursive calculation for ML with ML starting at ML of previous 100001 block (currently = ZM); Long term median

ML ; Dynamic penalty free zone.

MS = the median over the last 100 blocks of max(min(MB , 8ML) , ML) ; Effective short term median.

MN = MS ; Median for Penalty calculation.

RBase = Block Reward.

0 < MB ≤ 2MN, ; Requirement for valid block.

B = MB /MN - 1 where -1 < B ≤ 1

PB = RBaseB2 for B > 0 ; Monero applies a penalty PB, to increase the block weight by B; PB = 0 for B ≤ 0

Changes

1) Maximum growth of MS is reduced from 50ML to 8ML
3) Rate of growth and decline of ML is decreased from 1.7x to 1.2x
4) ZM is increased from 300000 bytes to 625000 bytes

2a) Minimum Fee For Node Relay (Old)

We add a, penalty attracting, transaction T with a size of TT to a block of weight MB

Define

TR = 3000 bytes ; Reference Transaction weight. Note: TR must be greater than T2. T2 equals the weight in bytes of a 2 input and 2 output transaction.

BT = TT / MN

PBT = RBase(B+BT)2 = Rbase( B2 + 2BBT + BT2 ) ; The new penalty, where B + BT > 0

PT = PBT – PB = RBase(2BBT + BT2 ) ; Increase in penalty from adding transaction T

FT = RBase(2BBT + BT2 ) ; The additional fee required to overcome the increase in penalty PT

For the case B = 0 this reduces to FT = RBaseBT2

MF = ML ; Median for minimum fee calculation
To calculate the minimum fee we consider a transaction of weight TR at the start of the penalty, B = 0 with MN = MF 95% of the fee required to pay the penalty incurred is the minimum fee.

BRL = TR / MF ;

FR = RBaseBRL2 ; Fee required to pay the penalty incurred

fR = RBaseBRL/MF ; Fee required to pay the penalty incurred per byte for a given MF

fI = 0.95fR ; Minimum fee per byte

2a) Minimum Fee For Node Relay (New)

We add a, penalty attracting, transaction T with a size of TT to a block of weight MB

Define

TR = 10000 bytes ; Reference Transaction weight. Note: TR must be greater than T2. T2 equals the weight in bytes of a 2 input and 2 output transaction.

BT = TT / MN

PBT = RBase(B+BT)2 = Rbase( B2 + 2BBT + BT2 ) ; The new penalty, where B + BT > 0

PT = PBT – PB = RBase(2BBT + BT2 ) ; Increase in penalty from adding transaction T

FT = RBase(2BBT + BT2 ) ; The additional fee required to overcome the increase in penalty PT

For the case B = 0 this reduces to FT = RBaseBT2

MF = ML ; Median for minimum fee calculation

To calculate the minimum fee we consider a transaction of weight TR at the start of the penalty, B = 0 with MN = MF 100% of the fee required to pay the penalty incurred is the minimum fee.

BRL = TR / MF ;

FRL = RBaseBRL2 ; Fee required to pay the penalty incurred

fRL = RBaseBRL/MF ; Fee required to pay the penalty incurred per byte for a given MF

fIL = fRL ; Minimum fee per byte

Changes

1) TR is increased from 3000 bytes to 10000 bytes. For clarity TR is defined outside of consensus.
2) There is no reduction to 95% of the minimum fee. This is all now handled on the wallet side.
2b) Wallet Fees (Old)

For the calculation of wallet fees we assume that the next 10 blocks have no transactions, other than the coinbase transaction, the empty blocks, We then calculate MLW and MSW by following the calculation of ML and MS at this future point. We use the previous 99990 blocks and the future 10 empty blocks (100000 blocks) for ML and the previous 90 blocks and future 10 blocks (100) blocks for MS.

Define

MBW = MB for the last 99990 blocks
MBW = 0 for the future 10 blocks; A value of 0 bytes can be used for the empty blocks for the purposes of calculating MLW.

MLW = The median over the last 99990 blocks and future 10 blocks (100000 blocks) of max((min (MBW , 2ML), ZM , ML/2) ; The current value of ML from consensus is used; Effective long term median for wallet fees

MLW ; Penalty free zone for wallet fees

MSW = the median over the last 90 blocks and future 10 blocks (100 blocks) of max(MBW , MLW); Effective short term median for wallet fees

MNW = min(MSW , 50MLW)

MFW = MLW ; Median for wallet fee calculation

BRLW = TR / MFW ; Used for the low and normal fees

BR = TR / ZM ; Used for the medium and high fees

FL = RBaseBRLW2 ; Low transaction fee for reference transaction

fL = RBaseBRLW/MFW ; Low transaction fee per byte for a given MFW

fN = 4fL ;Normal transaction fee per byte for a given MFW

fM = 16 RBaseBR/MFW ; Medium Transaction fee per byte for a given MFW

fP = 2RBase/MNW = fMMFW/(8BRMNW); Maximum Penalty (B =1) Transaction fee per byte for a given MNW

fH = 4fMmax (1, MFW/(32BRMNW)); High Transaction fee per byte

2b) Wallet Fees (New)

For the calculation of wallet fees we assume that the next 1000 blocks have no transactions, other than the coinbase transaction, the empty blocks, We then calculate MLW by following the calculation of ML at this future point. We use the previous 99000 blocks and the future 1000 empty blocks (100000 blocks) for ML.

Define

MBW = MB for the last 99000 blocks
MBW = 0 for the future 1000 blocks; A value of 0 bytes can be used for the empty blocks for the purposes of calculating MLW.

MLW = The median over the last 99000 blocks and future 1000 blocks (100000 blocks) of max((min (MBW , 2ML), ZM , ML/2) ; The current value of ML from consensus is used; Effective long term median for wallet fees

MLW ; Penalty free zone for wallet fees

MFW = MLW ; Median for wallet fee calculation

BRLW = TR / MFW ; Used for all fees

BR = TR / ZM ; Used for reference

FL = RBaseBRLW2 ; Low (minimum scaling) transaction fee for reference transaction

fL = RBaseBRLW/MFW ; Low (minimum scaling) transaction fee per byte for a given MFW

fN = 4fL ; Normal transaction fee per byte for a given MFW

fM = 16fL ; Medium Transaction fee per byte for a given MFW

fH64 = 64fL ; 64x Transaction fee per byte for a given MFW

fH256 = 256fL 256x Transaction fee per byte for a given MFW. This is greater than or equal to Maximum Penalty (B =1 ) for ML < 1280000 bytes.

Changes

1) All fees including the high fee are now based upon MLW
with the ratio between fees constant for a given MLW.
2) The grace period is increased to 1000 blocks.
3) 5 fee levels with at least a 4x factor between fees. Aditional fee levels can be added if needed at 1024x, 4096x etc. for larger ML
3) Consensus Transitional considerations for Minimum penalty free zone, ZM, and Median calculations after the fork.

Define:

ZMOld = 300000 bytes (ZM before hard fork)

MBOld = Block Weight in bytes (before hard fork)

3) Consensus Transitional considerations for Minimum penalty free zone, ZM, and Median calculations after the fork.

Calculation of ML, MS, MLW and MSW where blocks from a previous the Monero version are included in a calculation after the fork. MB is modified as follows:

Define

ZM = 625000 bytes

For blocks before the hard fork
MB = MBOld ( ZM / ZMOld )

The medians are then calculated normally.

4) Wallet Fee Rounding

Wallet fees, fN, fL, fM, and fH are rounded up to the desired
number of significant digits in the significant

Wallet Fee Rounding Examples

Two significant digits

27810	Rounded to : 28000
37.94	Rounded to : 38
0.5555	Rounded to : 0.56
0.002342	Rounded to : 0.0024
4) Wallet Fee Rounding

Wallet fees, fN, fL, fM, fH, and fX are rounded to 2 significant digits in the significant

Wallet Fee Rounding Examples

Two significant digits

27810	Rounded to : 28000
37.94	Rounded to : 38
0.5555	Rounded to : 0.56
0.002342	Rounded to : 0.0023